## Slide 1
CACHE REPLACEMENT POLICIES
LEAST FREQUENTLY USED
AND
MOST FREQUENTLY USED
COMPUTER ORGANIZATION AND ARCHITECTURE PROJECT

## Slide 2
Caches store frequently used data for faster access. When full, they need to evict something. Least Frequently Used (LFU) removes data accessed the least, while Most Frequently Used (MFU) (not common) removes the most accessed data first. LFU avoids a specific issue but adds tracking overhead. The best policy depends on your workload's access patterns.
ABSTRACT
1

## Slide 3
CACHE REPLACEMENT POLICIES
2
In computing, caches are temporary storage areas that hold frequently accessed data or instructions closer to the processor for faster retrieval. When a cache reaches its capacity and new data needs to be stored, a cache replacement policy determines which existing data to evict to make room. This decision significantly impacts the cache's effectiveness.
The replacement policy has to be chosen in such a way that the cache misses are reduced.

## Slide 4
CACHE REPLACEMENT POLICIES
3
We have discussed the following Cache Replacement policies
  First-In-First-Out (FIFO): The data item that has been in the cache the longest (the first one added) is evicted to make room for new data.
  Least Recently Used (LRU): The data item that has been accessed the least recently is evicted. This is a popular and effective policy that prioritizes keeping recently used data in the cache.
  Most Recently Used (MRU): (Less common) This policy, while not as widely used, evicts the data item that was most recently accessed. While it seems counterintuitive, MRU can be beneficial in specific scenarios.
  Random Replacement: A random data item is chosen for eviction. This is a simple but less effective policy.

## Slide 5
4
TRADITIONAL CACHE REPLACEMENT POLICY
In the traditional LRU policy, the victim block is chosen from the LRU position of the priority chain. The newly inserted block is placed in the MRU position and on a cache hit the cache block is promoted to the MRU position. As an example in the fig., on insertion of incoming block ’i’ in to the priority chain, the block at the LRU position ’g’ is removed from it and the insertion of block ’i’ occurs in the MRU position.

## Slide 6
5
A CACHE REPLACEMENT POLICY BASED ON RE-REFERENCE COUNT
The re-reference count refers to the number of times a cache block has been referenced since it was last brought into the cache. It helps track the recent usage pattern of cache blocks.
If the re-reference count exceeds a threshold, the cache block is promoted to the MRU position; otherwise, it remains at the LRU position.
The threshold mentioned in this context is a predetermined value based on set duelling, used to determine whether a cache block should be promoted to the MRU (Most Recently Used) position or remain at the LRU (Least Recently Used) position.
In set dueling some of the cache sets will be dedicated to follow LRU policy and some other sets will follow BIP policy and rest of the sets are known as follower sets. The follower sets choose that policy which incurs fewer misses in the above sets.

## Slide 7
6
A CACHE REPLACEMENT POLICY BASED ON RE-REFERENCE COUNT
In this technique, the promotion policy similar in case of LIP is modified in such a way that if the re-reference count is greater than a threshold value, the cache block is promoted on to the MRU position else it is promoted to LRU position as shown in fig.2. Results show that under this modification L2 cache miss rate can be reduced.

## Slide 8
7
A CACHE REPLACEMENT POLICY BASED ON RE-REFERENCE COUNT
Algorithm:
Input: SPEC CPU 2006 Benchmarks
Output: L2 Cache Miss Rate
1: for blocks undergone cache hit do
2: if blocks re-reference count > (14) then
3: Move to MRU position
4: else
5: Move to LRU position
6: end if
7: end for
8: for blocks need to be inserted to cache do
9: Move to LRU position
10: end for
11: for blocks to be evicted from the cache do
12: Select from LRU position
13: end for
For the memory intensive workload, when the re-reference count is set to 4, there is a significant reduction in L2 cache miss rate.
When the re-reference count is set to 14, there is a 60% improvement in L2 cache miss rate when compared to the traditional LRU policy.

## Slide 9
8
LEAST FREQUENTLY USED (LFU)
  Concept: The LFU policy prioritizes removing data items in the cache that have been accessed the least number of times overall. The assumption is that data accessed less frequently is less likely to be needed again soon.
  Implementation: LFU requires tracking access frequencies for each data item. This can be achieved using counters or timestamps. When a cache eviction is necessary, the item with the lowest access count is removed.

## Slide 10
9
Advantages:
  Can be effective for workloads with a mix of access patterns, particularly for data that becomes less relevant over time (e.g., web browsing history).
Disadvantages:
  Tracking access frequencies can add overhead, especially for large caches or frequent updates.
  May not be ideal for scenarios where recently accessed data might still be needed even if accessed infrequently overall.
LEAST FREQUENTLY USED (LFU)

## Slide 11
MOST FREQUENTLY USED(MFU)
10
  Concept: The MFU policy prioritizes removing data items in the cache that have been accessed the most number of times overall. The underlying idea is that data accessed more often is less likely to be needed again soon.
  Implementation: Similar to LFU, MFU also requires tracking access frequencies for each data item. This can be achieved using counters or timestamps. When a cache eviction is necessary, the item with the highest access count is removed.

## Slide 12
MOST FREQUENTLY USED(MFU)
11
Advantages :
  Aims to keep the less frequently accessed data in the cache, assuming it's more likely to be needed again soon.
Disadvantages :
  MFU has a problem when a recently accessed item is evicted just before it's needed again, leading to a cache miss.
  Tracking access frequencies incurs overhead.
LFU & MFU Implementation
https://github.com/nehakantheti/CacheReplacementPolicies.git

## Slide 13
CONCLUSION
12
We explored MFU (Most Frequently Used) and LFU (Least Frequently Used) cache replacement strategies. MFU aims to remove the most accessed data, but its implementation can be complex. LFU removes data accessed less often.
The best policy depends on your workload. If recent access is a strong indicator of future use, MFU might not be ideal. Consider well-established alternatives that balance recency and access frequency to optimize your cache's performance.

## Slide 14
REFERENCES
13
Referenced Paper :
A Cache Replacement Policy Based on Re-reference Count Sreya Sreedharan Department of Computer Science and Engineering Rajagiri School of Engineering and Technology Kochi, India
Referenced Site: IEEE Xplore

## Slide 15
THANK YOU
CS22B1020 Deshna Thunga
CS22B1081 Neha Kantheti
CS22B1082 Nimisha Thallapally